## Slide 1: EMAG Lab-2
Vector Analysis

## Slide 2: 2(A)
Three charges Q1= 1 micro , q2= 2 micro and q3=-3 micro is located at (1,3,0) , (4,2,0) and (0,0,1) respectively. Perform following function using Vector Analysis in MATLAB.
  Define three distance vectors joining Q1, Q2 and Q3 joining origin in Rectangular Co-ordinate Systems.
  Find out the direction of Force on Each charge due to Every other charge and unit vectors in that direction.
  Find out the distance between charges and Perimeter of the triangle.
  Find out the area of the triangle made by charge distribution.

## Slide 3: 2(B)
The vector electric field E= y ax -2.5x ay + 3 az and the point Q(4,5,2). Fine E at Q; the scalar component of E at Q in the direction of an = (1/3)*(2ax+ay-2az); the vector component of E at Q in the direction of an; and finally the angle between E(Q) and an.

## Slide 4: 2(C)
Show that the volume of a parallelopiped is defined by three vectors originating at a point can be defined in terms of the scalar and vector products of the vectors.

## Slide 5: 2(D)

## Slide 6
We can use MATLAB symbolic operations to express a vector field. The
symbolic operation is easy for students to understand and the student version
of MATLAB has the symbolic toolbox. Firstly, we define x, y and z as
symbolic variables using MATLAB command syms as
syms x y
And then we can write down vector field A as
A = [4*x^2, 2*x*y]
For the values of A at specific points, we can use MATLAB command subs to
obtain.
A_point1 = subs(A,{x,y},{1,-1})
A_point2 = subs(A,{x,y},{-2,3})
And the unit vectors can be obtained as
a_A1 = A_point1/norm(A_point1)
a_A2 = A_point2/norm(A_point2)

## Slide 7
(2) We can get the x component of A from
Ax = A(1);
To plot Ax using MATLAB function plot for x from –2 to 2, we need to
calculate numerical values of Ax as follows
xx = –1:0.1:1;
Axx = subs(Ax,{x},{xx});
And then, we can simply plot as follows
plot(xx,Axx);
(3) We can get Ay from
Ay = A(2) ;
To plot using surf, we need to build a mesh using MATLAB function
meshgrid.
[X, Y] = meshgrid(-1:0.1:1, -1:0.1;1)
And then, we calculate numerical values of Ay on this mesh using subs
Ay_num = subs (Ay, {x,y},{X,Y})
After that, we can plot Ay using 3D MATLAB plot function surf
surf(X,Y,Ay_num)

## Slide 8
We can also calculate Ax on the mesh although it only depends on x. That is,
Ax_num = subs (Ax, {x,y},{X,Y})
And then, the vector field A(x,y) can be plotted using quiver.
quiver(X,Y,Ax_num,Ay_num)
In quiver plot, the magnitude and direction of the vector field at any point are
indicated by the length and orientation of the arrows. In all the figures plotted,
we can add labels for all the axes and title for each figure.