## Slide 1: Emag Lab-3
Co-ordinate Systems

## Slide 2: Aim
To understand different types of co-ordinate systems in MATLAB and conversion between them.
  a. Write MATLAB functions to convert Rectangular co-ordinates and vectors into cylindrical and spherical co-ordinates and vectors.
  b. Write MATLAB functions to convert Cylindrical co-ordinates and vectors into Rectangular co-ordinates and vectors.
  c. Write MATLAB functions to convert spherical co-ordinates and vectors into rectangular co-ordinates and vectors.

## Slide 3: 3(a) Rectangular to cyllindrical co-ordinates
function Pcyl = car2cyl(Pcar)
x = Pcar(1);
y = Pcar(2);
z = Pcar(3);
rho = sqrt(x^2+y^2);
phi = atan2(y, x) ;
Pcyl = [rho, phi, z];
end

## Slide 4: For vectors
function Acyl = Scar2cyl(Acar)
syms rho phi z;
x = rho*cos(phi);
y = rho*sin(phi);
theta = atan(rho,z); % In case the input has theta. Acar = subs(Acar);
[K L] = size(Acar);
if (K*L) == 1 % scalar field
T = 1;
else if L == 1 % column vector field
Acar = Acar.';
end
T = [cos(phi) -sin(phi) 0; ... sin(phi) cos(phi) 0; ... 0 0 1];
end
Acyl = Acar*T;
Acyl = simplify(Acyl);
if L == 1 & K ~= 1
Acyl = Acyl.'; % if the input is column vector field
end

## Slide 5: For converting into spherical
function S = car2sph(R)
x = R(1);
y = R(2);
z = R(3);
r = norm(R);
rho = sqrt(x^2+y^2);
theta = atan2(rho,z);
phi = atan2(y,x);
S = [r,theta,phi];

## Slide 6: Exercises
Convert (2.57, -3.064,2) into cylindrical System. Ans: (4, -50deg, 2)
Transform 5 ax into cylindrical vectors at (4, 120deg, -1).
Convert F = [2xyz 0 -5(x+y+z)] in to cylindrical system.
Convert (2,3,-1) into spherical co-ordinate systems. (3.742, 105.5deg, 56.3deg)
Transform 5 ax into spherical system.

## Slide 7: Assignment
Find magnetic flux density on xoy plane (z=0) from a line current I on z axis from -a to a.