## Slide 1: Emag Lab-4
Electrical and Magnetic field plotting in Matlab

## Slide 2: 4(A)

## Slide 3
We can use MATLAB symbolic operations to express a vector field. The
symbolic operation is easy for students to understand and the student version
of MATLAB has the symbolic toolbox. Firstly, we define x, y and z as
symbolic variables using MATLAB command syms as
syms x y
And then we can write down vector field A as
A = [4*x^2, 2*x*y]
For the values of A at specific points, we can use MATLAB command subs to
obtain.
A_point1 = subs(A,{x,y},{1,-1})
A_point2 = subs(A,{x,y},{-2,3})
And the unit vectors can be obtained as
a_A1 = A_point1/norm(A_point1)
a_A2 = A_point2/norm(A_point2)

## Slide 4
(2) We can get the x component of A from
Ax = A(1);
To plot Ax using MATLAB function plot for x from –1 to 1, we need to
calculate numerical values of Ax as follows
xx = –1:0.1:1;
Axx = subs(Ax,{x},{xx});
And then, we can simply plot as follows
plot(xx,Axx);
(3) We can get Ay from
Ay = A(2) ;
To plot using surf, we need to build a mesh using MATLAB function
meshgrid.
[X, Y] = meshgrid(-1:0.1:1, -1:0.1;1)
And then, we calculate numerical values of Ay on this mesh using subs
Ay_num = subs (Ay, {x,y},{X,Y})
After that, we can plot Ay using 3D MATLAB plot function surf
surf(X,Y,Ay_num)

## Slide 5
We can also calculate Ax on the mesh although it only depends on x. That is,
Ax_num = subs (Ax, {x,y},{X,Y})
And then, the vector field A(x,y) can be plotted using quiver.
quiver(X,Y,Ax_num,Ay_num)
In quiver plot, the magnitude and direction of the vector field at any point are
indicated by the length and orientation of the arrows. In all the figures plotted,
we can add labels for all the axes and title for each figure.

## Slide 6: 4(B)
Plot vector magnetic field Intensity in Cartesian co-ordinates on xy plane caused by a current filament of 1 A in the z direction and extending from z=-1 to 1.

## Slide 7
syms x y z_prime real
syms a I PI mu0 positive
a_z = [0 0 1];
r = [x y 0];
r_prime = [0 0 z_prime];
R = r-r_prime;
norm_R = sqrt(R(1)^2+R(2)^2+R(3)^2);
a_R = R/norm_R;
dH = cross(a_z,a_R)/norm_R^2
disp('Magnetic field Intensity in Cartesian system')
HH = int(dH,z_prime); I = 1;
H = (subs(HH,z_prime,1) - subs(HH,z_prime,-1))*I/4/pi
ezsurf(H);

## Slide 8: Assignment
Find the vector magnetic field intensity in cartesian co-ordinates at P(1.5,2,3) caused by current filament of 24A in the az direction on the z axis and extending from: z=0 to z=6.
Ans: -0.939ax + 0.704 ay A/m